## Slide 1: Design of a 4-bit Simple As Possible (SAP) Computer
Course Instructor:
Dr. A.B.M. Harun-Ur-Rashid Rifat Shahriar
Professor, Department of EEE, BUET Lecturer, Department of EEE, BUET
Prepared By:
Ramit Dutta Shafin Bin Hamid
ID: 1606006 ID: 1606008
Course No: EEE 458
Course Name: VLSI Circuits and Design II Laboratory

## Slide 2: Outline
Discussion of design criteria and basic building blocks
Demonstration of functional verification using EDA Playground
Simulation using Cadence NC-Sim and Sim Vision
RTL logic synthesis using Cadence Genus
Physical design using Cadence Innovus
Investigation of Design Rules Check (DRC) errors

## Slide 3: Design Route
Testbench
Program Counter Testbench
MAR Testbench
RAM Testbench

## Slide 4: Design Route
Build a Control Sequencer to generate control signals for synchronization
Control Sequencer is the brain of the computer because it controls which modules are active/inactive
Control signals are generated at the negedge
The operation based on the control signal happens on the next posedge
Need to make all the modules work synchronously
So everything happens as and when they are required to do so

## Slide 5: Final Design
RAM Size is 16 * 8
First 9 locations contain instructions
Next 7 locations are for storing data
Instruction length is 8 bits
Data length is 4 bits
For data, first 4 bits are set to zero
First 4 bits of instruction are opcode, second 4 bits are operand
For instructions that do not have a valid operand, last 4 bits are set to zero
All ALU operations are done with 4-bit registers

## Slide 6: Instruction Set
Instruction | Operation | Opcode
LDA Address | Load the accumulator with the content located at the specified address of RAM | 0000
ADD Address | Add to the accumulator the content located at the specified address of RAM | 0001
SUB Address | Subtract from the accumulator the content located at the specified address of RAM | 0010
OUT | Display the content of the output register | 1110
HLT | Halt program execution (stops the program counter from incrementing) | 1111

## Slide 7: Demonstration of the Computer
Assembly Code
LDA 9h ;move RAM[9] to A
ADD Ah ;add RAM[10] to A
OUT ;display A
SUB Ah ;subtract RAM[11] from A
OUT ;display A
ADD Ah ;add RAM[10] to A
HLT ;halt program execution
RAM Index | RAM Content at Index
0 | 0000_1001
1 | 0001_1010
2 | 1110_0000
3 | 0010_1011
4 | 1110_0000
5 | 1111_0000
6 | 0001_1010
7 | 1110_0000
RAM Index | RAM Content at Index
9 | 0000_1011
10 | 0000_0001
11 | 0000_0011
Conversion to machine code and mapping
Data Segment
OUT ;display A

## Slide 8: Demonstration of the Computer
Generation of control signals resemble ring counter
Control signal generation occurs at negedge clock
Data transfer occurs at next posedge clock
A=11 at the end of first instruction cycle
LDA 9h

## Slide 9: Demonstration of the Computer
OUT
First three T states are similar
A sends data to output register

## Slide 10: Demonstration of the Computer
ADD Ah
RAM[10] goes to B
ALU Computes A+B
A=Ch
OUT

## Slide 11: Demonstration of the Computer
SUB Bh
RAM[11] goes to B
ALU Computes A-B
A=9h
OUT

## Slide 12: Demonstration of the Computer
HLT
Program counter value is indefinitely set to 6.
PC keeps fetching the same instruction

## Slide 13: Challenges of multiple modules
Due to the usage of multiple modules, our design could not be synthesized all at once
We can synthesize each module separately, but if we try to synthesize using multiple modules, then the netlist file remains blank
To solve this situation, we converted the code into a single module
The inputs are clock, reset, input mode, input addresses and input instructions
The output is a 4 bit data output that is to be displayed from the output register
From here on, all results will be discussed based on aforementioned inputs and outputs

## Slide 14: Simulation using Cadence NC-Sim and Sim Vision – Inputs

## Slide 15: Simulation using Cadence NC-Sim and Sim Vision – LDA+OUT Testbench

## Slide 16: Simulation using Cadence NC-Sim and Sim Vision – ADD+OUT Testbench

## Slide 17: Simulation using Cadence NC-Sim and Sim Vision – SUB+OUT Testbench

## Slide 18: Simulation using Cadence NC-Sim and Sim Vision – HALT Testbench

## Slide 19: Schematic

## Slide 20: Power Report

## Slide 21: Timing Report

## Slide 22: Physical Design - Floorplan
Floorplan parameters:
Die size is 100 by 100
Total number of input pins = 15
Total number of output pins = 4
Input pins spacing = 5
Output pins spacing = 20
Pinwidth = 0.14
Pindepth = 0.28
Core to left/right = 3
Core to top/bottom = 5

## Slide 23: Physical Design – Design Browser

## Slide 24: Physical Design – Adding power stripe & routing
Power Stripe:
Metal4 layer is used
Width of each strip = 0.5
Spacing between VDD and VSS = 2
Set to set distance = 5
First strip starts a distance 3 away from left core boundary
Route:
For top layer, Metal4 layer is used
For bottom layer, Metal1 is used

## Slide 25: Physical Design – Adding optimum design

## Slide 26: Physical Design – Report Timing
Slack time is positive and less than the required time

## Slide 27: Physical Design – Geometry Verification

## Slide 28: Physical Design – After Metal Fill
All the filler cell libraries are selected to avoid DRC errors later

## Slide 29: Physical Design – Connectivity Verification

## Slide 30: Physical Design – Geometry Verification

## Slide 31: Physical Design – Layout at Virtuoso

## Slide 32: Physical Design – DRC Error

## Slide 33: Terminologies of DRC errors
NIMP.SP.1  Minimum N+ Implant Space >= 0.12 um
PIMP.SP.1  Minimum P+ Implant Space >= 0.12 um
NW.SP.1  Minimum N-well spacing to N-well (same potential) >= 0.3um
NW.W.1  Minimum N-well width >= 0.3um
Offgrid check  Drawn layer is not aligned with the grid settings

## Slide 34: Terminologies of DRC errors(Cont’d)
VIA1.E.3  At least 2 Via1 must be used to join Metal1 and Metal2 when they are within 3.0 um of a metal plate(Metal1/Metal2) when the metal plate size has width>1.5 and length> 1.5
VIA2.E.3  At least 2 Via2 must be used to join Metal2 and Metal3 when they are within 3.0 um of a metal plate(Metal2/Metal3) when the metal plate size has width>1.5 and length> 1.5
VIA3.E.3  At least 2 Via3 must be used to join Metal23and Metal4 when they are within 3.0 um of a metal plate(Metal3/Metal4) when the metal plate size has width>1.5 and length> 1.5

## Slide 35: Trial and Error
Case No | Physical Design Parameter | DRC Errors | Comment
1 | Die Size : 100*100 Input pin spacing : 2 Output pin spacing : 5 Other design parameters are followed from lab-sheet | NIMP.SP.1  34 NW.SP.1  29 NW.W.1  5 PIMP.SP.1  31 offgrid_check  98 | Total Error = 196 Offgrid check error due to Geometry Violation error
2 | Same Die Size, Input pin spacing & Output pin spacing Core to IO boundary: Core to Left/Right : 3 Core to Top/Bottom : 4.94 Power Stripe Width : 0.5 Power Stripe Spacing : 2 First Power Stripe (X from Left) : 3 | NIMP.SP.1  39 NW.SP.1  26 NW.W.1  2 PIMP.SP.1  35 VIA1.E.3  1 VIA2.E.3  2 VIA3.E.3  1 | Total Error = 106 offgrid_check errors are gone but VIA errors are introduced

## Slide 36: Trial and Error(Cont’d)
Case No | Physical Design Parameter | DRC Errors | Comment
3 | Die Size : 100*100 Input pin spacing : 5 Output pin spacing : 20 Other design parameters are followed from case 2 | NIMP.SP.1  25 NW.SP.1  25 NW.W.1  6 PIMP.SP.1  29 | Total Error = 85 VIA errors are gone
4 | Die Size : 200*150 Other design parameters are followed from case 2 | NIMP.SP.1  19 NW.SP.1  11 NW.W.1  9 PIMP.SP.1  14 | Total Error = 43 Spacing error decreases but well error increases
5 | Die Size : 200*150 Other design parameters are followed from case 4 & adding all the filler cell | 0 | Total Error = 0 All errors are gone
6 | Die Size : 100*100 Other design parameters are followed from case 3 & adding all the filler cell | 0 | Total Error = 0 All errors are gone

## Slide 38: Appendix
EDA Playground Link : https://www.edaplayground.com/x/W42N
The nomenclature of DRC is errors is taken from gpdk045_drc library provided by Cadence Design Systems. Link to pdf: https://perso.telecom-paristech.fr/mathieu/ICS904_TP_LAYOUT/html/_static/doc/gpdk045_drc.pdf